## Slide 1: Basic Electrical Safety for Industrial Workers
Test Training Institute

## Slide 2: Unit 1: Understanding Electrical Hazards
Live conductors >50 V AC/DC – keep ≥2 m clearance
Damaged insulation or exposed wiring = shock risk
Arc‑flash can exceed 20 000 °C – wear flash suit
Safety labels: ‘High Voltage’, ‘Lock‑out/Tag‑out’, colour‑coded symbols
Notes: When we walk the floor we must stay at least two metres from any live conductor above 50 V, as required by the OHSA. A typical shock source is a frayed power cord on a welding machine, which caused an emergency stop last month. Always verify the red high‑voltage triangle and lock‑out/tag‑out tags before beginning work.

## Slide 3: Unit 2: Personal Protective Equipment (PPE)
Match voltage class: use arc‑flash rated gloves & insulated tools for >1 kV work
Inspect PPE each shift: check for tears, cracks, missing tags, and expiry dates
Know limits: PPE won't protect against chemical burns, >200 °C heat, or impacts beyond its rating
Notes: When beginning any live‑work task, first match the voltage class to the PPE – for example, on a 3 kV switchgear job we wear class 2 insulated gloves and a dielectric mat. Before putting them on, conduct a quick visual and tactile inspection for cuts, worn seams, and verify the certification tag is current; any defect means you must replace the item. Keep in mind PPE only reduces risk; it won’t stop burns from hot surfaces above its temperature rating, so always combine it with lock‑out/tag‑out and other safe work practices.

## Slide 4: Unit 3: Safe Isolation Procedures
Identify and isolate ALL energy sources before any work begins
Apply lockout device and tag with your unique ID – never remove another's lock
Use a calibrated tester to confirm zero voltage/current before starting
Record the isolation step and inform all affected personnel
Comply with MERSETA LOTO regulations – non‑compliance can lead to fines and prosecution
Notes: Explain that each lockout must match the specific energy source and that only the person who applied the lock may remove it. Demonstrate with a real‑world example: on a metal‑stamping line, the maintenance technician locks out the main motor, tags it with his ID, then uses a multimeter to verify no voltage before opening the guard. Remind learners that proper documentation and communication protect both workers and the company from legal penalties.

## Slide 5: Unit 4: Emergency Response
Cut power at the source before approaching the victim
Use insulated gloves and non‑conductive tools; never touch a live person
Check responsiveness, call emergency services, then start CPR if needed
Document the incident and report to the safety officer within 24 hrs
Notes: If you hear a spark or see someone collapse, immediately isolate the electricity by switching off the breaker or unplugging the equipment, then use a dry, non‑conductive object to move the source away before providing aid. For example, when a technician was shocked by a faulty drill in our workshop, the team turned off the mains, used a wooden pole to remove the drill, and began CPR while awaiting the ambulance. After the emergency, record all details and notify the safety officer within 24 hours.