## Slide 1: Basic Electrical Safety for Industrial Workers
Test Training Institute

## Slide 2: Unit 1: Understanding Electrical Hazards
Live parts ≥ 50 V AC / 30 V DC exposed or poorly insulated
Damaged cords, broken plugs & missing earth = leading shock causes
Warning symbols: IEC lightning bolt, burn symbol, and ‘Risk of electric shock’ labels
Lock‑out/Tag‑out (LOTO) required before any maintenance on energized equipment
Maintain a 1 m clearance around overhead power lines in the plant
Notes: Electrical hazards are everywhere in an industrial site – for example, a weld‑shop worker once received a shock because a frayed welding cable was left coiled near a metal workbench. Emphasise that any live part above 50 V AC must be protected, that damaged insulation is the top cause of shocks, and that clear warning symbols and proper LOTO procedures prevent incidents.

## Slide 3: Unit 2: Personal Protective Equipment (PPE)
Choose insulated, flame‑resistant gloves rated ≥1000 V for live work
Perform a pre‑use visual check: look for tears, cracks, worn seams, and test for electrical continuity
Use hard hats with a dielectric rating and pair with face shields that meet ANSI Z87.1 for arc flash
PPE protects against hazards, not eliminates them – maintain safe distances and lock‑out/tag‑out
Replace PPE that shows damage or exceeds its service life (e.g., 5 years for rubber gloves)
Notes: When starting on a live panel, match PPE to the voltage – for example, use insulated gloves rated at 1000 V or higher for work on an 11 kV breaker. Before wearing them, do a quick visual and continuity check; if a nick or test failure is found, replace the glove immediately. Remember, PPE is the last line of defence – in our plant an electrician spotted a cracked glove before servicing a breaker and avoided a shock incident.

## Slide 4: Unit 3: Safe Isolation Procedures
Follow the 5‑step LOTO sequence: Identify, Notify, Isolate, Lockout, Verify
Verify zero energy with a calibrated tester before starting work
Document each lockout with a tag that includes the worker’s name, date & time
Legal: OHS Act 85/1993 & Regulations require written isolation procedures and impose penalties up to R1 million
Notes: Explain that the five‑step LOTO process is the backbone of safe isolation, and that a live test with a properly calibrated meter is the final safeguard. For example, before repairing a conveyor motor, the electrician shuts off the breaker, applies his lock, tags it, then confirms zero voltage with a multimeter before beginning work.

## Slide 5: Unit 4: Emergency Response
Turn off the circuit breaker or isolate the source before any rescue.
Never touch a shocked person with bare hands – use insulated tools or a wooden stick.
Assess: unconscious or severe burn → call 112 immediately; otherwise administer CPR/first aid.
If the victim shows cardiac arrest or burns > 2% body surface, escalate to emergency services without delay.
Notes: When a coworker receives an electric shock, the first priority is to cut the power and avoid becoming a second victim; for example, an electrician who was shocked on a live panel was rescued by a colleague who used a dry wooden pole to move the victim after isolating the breaker. After the source is secured, quickly check responsiveness – if they're unconscious or have major burns, call 112 and start CPR while another person prepares an AED.